## Slide 1
Platelet Guidance
Bacterial Risk Control Strategies
Christine Hayes, COO/VP of Operations
Abby Huntrods, Director of Hospital Services
Rachael Muhs, Technical Services Supervisor
Dr. Alex Smith, Medical Director

## Slide 2
Background
Platelet Transfusion Bacterial Risk
Room Temp platelets associated with higher sepsis risk and related fatalities
Bacterial contamination of platelets is leading infection risk from transfusions
Depending on the source and surveillance method, there are about 1/10,000 to 1/100,000 transfusion-transmitted infections per year from platelets.
Evidence of 1 in 6,000 products suspected to have infectious agent
The highest risk of a transfusion-transmitted infection occurs in platelets that are at days 4 to 5 of their shelf life, with 95 to 100% of septic transfusion reactions occurring on these days, and 100% of fatalities in the same range.
Risk has continued with implementation of single culture ≥24 hours

## Slide 3
Food and Drug Administration (FDA)
Platelet Bacterial Guidance
FDA has established regulations to address the control of bacterial contamination of platelets. Under 21 CFR 606.145(a), blood establishments and transfusion services must assure that the risk of bacterial contamination of platelets is adequately controlled using FDA approved or cleared devices, or other adequate and appropriate methods found acceptable for this purpose by FDA. Implementation by March 31, 2021
Recommendations to control the risk of bacterial contamination applies to:
Room temperature stored platelets intended for transfusion
Apheresis and Whole Blood derived platelets
Single Donor Platelets and Acrodose pools
Platelets in plasma and preservative

## Slide 4
Food and Drug Administration (FDA)
Platelet Bacterial Guidance
To read the full guidance, follow link below:
“Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion “

## Slide 5: Available Testing Strategies Overview
Single Step Strategies:
  Large Volume, Delayed Sampling (LVDS) ≥36 hours
  Large Volume, Delayed Sampling (LVDS) ≥48 hours
  Pathogen Reduction
Two-Step Strategies:
  Step 1: Primary Culture ≥24 hours
  or
  Large Volume, Delayed Sampling (LVDS) ≥36 hours
  Step 2: Secondary Culture
  or
  Secondary Rapid Testing (Verax)

## Slide 6: Product Shelf Life Comparisons

## Slide 7
Large Volume, Delayed Sampling LVDS 36 (no sooner than 36 Hours)
Single culture sampled no sooner than 36 hours after collection
Single-step strategy
Inoculate both aerobic and anaerobic cultures
Minimum sample volume 16 mL
Sample each apheresis or pre-storage pool
  Each split from a unit should be sampled
Minimum incubation 12 hours prior to release
5 day product expiration (48 hour hold time)
  Can be extended beyond 5 days with 2-step strategy

## Slide 8
Large Volume, Delayed Sampling LVDS 36 (no sooner than 36 Hours)
Advantages:
Does not hold product as long as LVDS 48
Secondary testing (Verax) can be applied
Lower Cost than Pathogen Reduction
Applicable to Acrodose products
No additional licensure submission
Disadvantages:
Impact to available inventory
    Holds product longer than Pathogen Reduction
Testing the product and not treating the product

## Slide 9
Large Volume, Delayed Sampling LVDS 48 (no sooner than 48 Hours)
Single culture sampled no sooner than 48 hours after collection
Single-step strategy
Inoculate both aerobic and anaerobic cultures
Minimum sample volume 16 mL
Sample each apheresis platelet
  Each split from a unit should be sampled
Minimum incubation 12 hours prior to release
7 day product expiration (60 hour hold time)

## Slide 10
Large Volume, Delayed Sampling LVDS 48 (no sooner than 48 Hours)
Advantages:
More likely to detect infectious agent with additional growth time
Lower Cost than Pathogen Reduction
7-Day Product
Disadvantages:
Impact to available inventory
  Holds product longer than Pathogen Reduction
Testing the product and not treating the product
Cannot use on Acrodose
Not available for secondary testing (Verax)
Licensure Submission (12-Month)

## Slide 11
Pathogen Reduction
Psoralen/UVA Light Treatment
  Targets DNA & RNA to prevent proliferation of pathogens
  Replacement for primary and secondary bacterial culture screening
  Approved alternative to Gamma Irradiation to prevent transfusion associated graft vs. host disease
Apheresis platelets
Currently 5 day expiration (developing 7 day expiration)

## Slide 12
Pathogen Reduction
Psoralen/UVA Light Treatment
  Advantages:
  Product Availability – Early Release, Optimal Shelf-Life
  Treating vs. Testing (No False Positive Product Loss)
  No documented Septic Transfusion Reaction
  Replaces Irradiation
  Replaces CMV testing
  Preparation of emerging infectious agents
  Possible long-term elimination of other testing (cost savings)
    Zika
    Babesia

## Slide 13
Pathogen Reduction
Psoralen/UVA Light Treatment
  Disadvantages:
  5 Day Product (future development of 7 day)
  Licensure Submission
  Inventory Issues (Dual Inventory)
  Hospital Acceptance of products for varied demographics
  Higher Cost Associated

## Slide 14
Secondary Rapid Testing
Verax Prime
  Two-Step 36 hour LVDS secondary testing
  Extends Expiration from 5 days up to 7 days
  Single Donor Platelet Tested at 72 hours and 96 hours
  Pooled Platelet tested at 72 hours only
  New Product Codes
  *LifeServe has been using this method since October 2019

## Slide 15
Secondary Rapid Testing
Verax Prime
  Advantages:
  Extended product availability
  Disadvantages:
  Products returned for secondary testing

## Slide 16: Comparison Overview
Pathway | Single Donor | Single Donor Expiration | Pooled | Pooled Expiration | License Submission
1 Step >36 Hours LVDS | Yes | 5 Days 48 Hour Hold | Yes | 5 Days 48 hour hold | No
1 Step >48 Hours LVDS | Yes | 7 Days 60 Hour Hold | No | N/A | Yes
2 Step >36 Hours LVDS Day 3 & 4 | Yes | 5 Days Tested at 72 hours & 92 Hours | Yes | 5 Days Tested at 72 hours | No
2 Step >36 Hours Day 4 Only | Yes | 7 Days Tested at 92 Hours | No | N/A | No
Pathogen Reduction | Yes | 5 Days 24 Hour Hold | No | N/A | Yes

## Slide 17: LifeServe Testing Strategy Decision
Combination of Single Step Strategies:
  Large Volume, Delayed Sampling (LVDS) ≥36 hours
  Large Volume, Delayed Sampling (LVDS) ≥48 hours
  Continued use to Verax for product life extension
  Continued investigation of Pathogen Reduction technology based on input from hospital customers

## Slide 18
Cost Considerations
All platelet product pricing will increase based on the method of additional, required testing.
Cost will be added to base price of product
  $83 Fee for all platelet products
Pathogen Reduction
    Anticipate increase cost of approximately $150/product
    *Pricing not guaranteed if imported per hospital request
    Your input will help us decide how and when we begin providing pathogen reduced products at LifeServe

## Slide 19
Next Steps
To follow adherence to guidance, implementation will occur no later than March 1, 2021
LifeServe License Submission for 48 hour LVDS
Formal Communication will be sent with pricing changes by Nov 1, 2020
Provide new product Codes for 48 hour LVDS products
Complete Survey

## Slide 20
Questions
Rachael Muhs, MLS (ASCP)
LifeServe Blood Center O+ Technical Services Supervisor
431 East Locust St | Des Moines, IA 50309
Telephone: 515-309-4947
Rachael.Muhs@lifeservebloodcenter.org
K. Alex Smith, DO
LifeServe Blood Center B+ Medical Director
431 E Locust St | Des Moines, IA 50309
Telephone: 515.309.4872
Fax: 515.243.2880
Alex.Smith@lifeservebloodcenter.org

## Slide 21
Thank you!

## Slide 22
Pre-Presentation Survey
Follow link to submit survey answers:
https://app.smartsheet.com/b/form/a211f1903c7a4de4a06f6117d7d7aae6
Do you understand that LifeServe Blood Center is required to follow the FDA guidance to integrate these changes?
Are you familiar the FDA Platelet Guidance located here(link)?
Has your facility discussed or made decisions on your preferred strategy to adhere to the guidance?
Would you like additional education opportunities provided specific to Pathogen Reduction?
Are you concerned additional required bacterial testing will impact your access to products?
Will you attend webinar?

## Slide 23: Post – Presentation Survey Follow link to submit survey answers: https://app.smartsheet.com/b/form/d6e9ce428dd342838e8422d4921a65b7
Did we answer your questions concerning the FDA’s new platelet guidance?
Do you believe that Pathogen Reduction provides a safer product than other bacterial detection methods?
Do you believe an additional increased cost associated with Pathogen Reduction is worth the added value of treating vs testing the product? Do you believe your hospital would be interested in obtaining pathogen reduced products?
Do you want additional opportunities to further discuss Pathogen Reduction?
Do you have additional questions?
Are you interested in educational opportunities in other topics?